## Slide 1
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION
Flask
↓
QC – Seed Qualification (Flask Stage)
Parameters Checked:
• PAR (light intensity)
• pH
• Microscopy observation (morphology, contamination)
• Cell count
• OD
• Cell size
• Automation (timers, light, aeration if applicable)
↓
Decision:
✔ QC Pass → Proceed to PBR 25 L
✖ QC Fail → Hold / Terminate / Restart batch
1. Flask Stage – Seed Culture Initiation

## Slide 2
PBR 25 L (Seed Reactor)
↓
QC – Seed Acceptance (25 L)
Parameters Checked:
• PAR
• pH
• Microscopy observation
• Cell count
• OD
• Cell size
• Automation
• Dry weight
↓
Decision:
✔ QC Pass → Scale-up to PBR 275 L
✖ QC Fail → Hold / Corrective action / Harvest (if required)
2. PBR 25 L – Seed Reactor
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION

## Slide 3
PBR 275 L (Intermediate Scale)
↓
QC – Contamination & Growth Check (275 L)
Parameters Checked:
• PAR
• pH
• Microscopy observation (CRITICAL checkpoint)
• Cell count
• OD
• Cell size
• Automation
• Dry weight
• Assay (if entering stress / red phase)
↓
QC DECISION GATE – 1
Contamination detected?
├─ YES → Reddening → Harvest
└─ NO → Proceed to PBR 925 L
3. PBR 275 L – Intermediate Scale
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION

## Slide 4
PBR 925 L (Seed Reactor)
↓
QC – Seed Release for Production (925 L)
Parameters Checked:
• PAR
• pH
• Microscopy observation
• Cell count
• OD
• Cell size
• Automation
• Dry weight
↓
QC DECISION GATE – 2
Contamination detected?
├─ YES → Reddening → Harvest
└─ NO → Proceed to PBR 6600 L
4. PBR 925 L – Large Seed Reactor
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION

## Slide 5
PBR 6600 L (Production Reactor)
Green Phase → Red Phase
↓
QC – Production Monitoring (6600 L)
Parameters Checked:
• PAR (phase-specific)
• pH
• Microscopy observation
• Cell count
• OD
• Cell size
• Automation
• Dry weight
• Assay (CRITICAL for harvest decision)
↓
Decision:
✔ Target dry weight & assay achieved → Harvest
✖ Not achieved → Continue cultivation / adjust conditions
Harvesting
↓
QC – Pre-Harvest & Post-Harvest
Parameters Checked:
• Dry weight
• Assay
5. PBR 6600 L – Production Reactor
6. Harvesting
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION

## Slide 6
Drying
↓
QC – Dried Biomass Release
Parameters Checked:
• Dry weight
• Assay
7. Drying
8. Packing (Bulk Biomass)
Packing
↓
QC – Packing Release
• Label verification
• Batch integrity
• COA linkage
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION

## Slide 7
Dispatch for External Extraction
↓
Receipt of Extracted Material
↓
QC – Incoming Material
Parameters Checked:
• Assay
• Physical inspection
• COA verification
↓
Re-Packing
↓
Final Dispatch
9. External Extraction & Supply Chain
ONE-LINE ERP / AUDIT VIEW
Flask → QC → 25L → QC → 275L → QC → 925L → QC → 6600L → QC → Harvest → Dry → Pack → Dispatch → Receive → Repack → Dispatch
END-TO-END PROCESS FLOW –BIOMASS PRODUCTION