## Slide 1
OVERALL PROCESS FLOW WITH IN-PROCESS PARAMETERS
1. Flask Stage (Seed Culture Initiation)
Flask ↓
QC – Seed Qualification (Flask Stage)
Parameters Checked:
PAR (light intensity setting)
pH
Microscopy Observation (cell morphology, contamination)
Cell Count
OD
Cell Size
Automation (timers, light control, aeration if applicable)
↓
Decision: ✔ QC Pass → Proceed to 25 L ✖ QC Fail → Hold / Terminate / Restart batch
2. PBR 25 L – Seed Reactor
PBR 25 L (Seed Reactor) ↓
QC – Seed Acceptance (25 L)
Parameters Checked:
PAR
pH
Microscopy Observation
Cell Count
OD
Cell Size
Automation
Dry Weight
↓
Decision: ✔ QC Pass → Scale-up to 275 L ✖ QC Fail → Hold / Corrective Action / Harvest (if required)
3. PBR 275 L – Intermediate Scale
PBR 275 L (Intermediate Scale) ↓
QC – Contamination & Growth Check (275 L)
Parameters Checked:
PAR
pH
Microscopy Observation (critical contamination checkpoint)
Cell Count
OD
Cell Size
Automation
Dry Weight
Assay (if entering stress / red phase)
↓
QC DECISION GATE – 1
Contamination Detected?
├─ YES → Reddening → Harvest
└─ NO → Proceed to 925 L

## Slide 2
OVERALL PROCESS FLOW WITH IN-PROCESS PARAMETERS
4. PBR 925 L – Large Seed Reactor
PBR 925 L (Seed Reactor) ↓
QC – Seed Release for Production (925 L)
Parameters Checked:
PAR
pH
Microscopy Observation
Cell Count
OD
Cell Size
Automation
Dry Weight
↓
QC DECISION GATE – 2
Contamination Detected?
├─ YES → Reddening → Harvest
└─ NO → Proceed to 6600 L
5. PBR 6600 L – Production Reactor
PBR 6600 L (Production – Green Phase → Red Phase) ↓
QC – Production Monitoring (6600 L)
Parameters Checked (Green & Red Phase):
PAR (phase-specific)
pH
Microscopy Observation
Cell Count
OD
Cell Size
Automation
Dry Weight
Assay (critical for harvest decision)
↓
Decision: ✔ Target DW & Assay achieved → Harvest ✖ Not achieved → Continue cultivation / adjust conditions
6. Harvesting
Harvesting ↓
QC – Pre-Harvest & Post-Harvest
Parameters Checked:
Dry Weight
Assay

## Slide 3
OVERALL PROCESS FLOW WITH IN-PROCESS PARAMETERS
7. Drying
Drying ↓
QC – Dried Biomass Release
Parameters Checked:
Dry Weight
Assay
8. Packing
Packing (Bulk Biomass) ↓
QC – Packing Release
Label verification
Batch integrity
COA linkage
9. External Extraction & Supply Chain
Dispatch for External Extraction ↓ Receipt of Extracted Material ↓
QC – Incoming Material
Parameters Checked:
Assay
Physical inspection
COA verification
↓
Re-Packing ↓
Final Dispatch